## Slide 1: Week 4 – Network and WIFI Security

## Slide 2: TCP/IP Model
defines 4 layers:
  Application Layer
    FTP, HTTP, DNS, SMTP, …
  Host-to-Host Transport Layer
    TCP, UDP
  Internet Layer
    IP, ARP, ICMP
  Network Link Layer
    Ethernet
Session Layer
Presentation Layer
Transport Layer
Network Layer
Application Layer
Physical Layer
Data Link Layer
OSI Model
Transport Layer
Network Layer
Application Layer
Data Link Layer
TCP/IP Model

## Slide 3: Ethernet Frame
Frame format

## Slide 4: MAC Addresses
ISO/IEC 8802 standard
Every Ethernet Network Card has a 6 Bytes MAC addresses
Each manufacturer has their own 3-bytes Organizational Unique Identifier (OUI)
https://standards.ieee.org/develop/regauth/oui/public.html

## Slide 5: Ethernet Illustration

## Slide 6: Internet Protocol (IP)
unreliable, connectionless datagram delivery
provide host-to-host data delivery
  “Routing”
map all hosts in the network an IP address (32-bits)

## Slide 7: IPv4
IP (Datagram) Header Format

## Slide 8: IP Illustration

## Slide 9: Internet Control Messages Protocol (ICMP)
Code | Description | Type
0 | Echo Reply | Query
3 | Destination Unreachable | Error
5 | Redirect | Error
8 | Echo request | Query
11 | Time exceeded | Error
13/14 | Timestamp request/reply | Query
Contains error messages and other conditions that require attention

## Slide 10: ICMP
ICMP Header Format

## Slide 11: ICMP Illustration

## Slide 12: Address Resolution Protocol (ARP)
Map between address of internet layer and network link layer
Dynamic / Static
  Broadcast for address resolution
32-bit Internet Address
48-bit Ethernet Address
ARP
RARP
Sample ARP cache

## Slide 13: ARP
ARP Request/Reply Packet

## Slide 14: ARP Illustration

## Slide 15: User Datagram Protocol (UDP)
simple, datagram-oriented
  Each output operation by a process produces exactly one UDP datagram
fast
unreliable
source ports dynamically assigned, > 1023

## Slide 16: UDP
UDP Header Format

## Slide 17: UDP Illustration

## Slide 18: Transport Control Protocol (TCP)
full-duplex, connection-oriented, reliable, virtual circuit
slower than UDP
reliable data transport:
  received a segment -> sent an acknowledge
  unacknowledged segment -> retransmitted
  segments sequenced back in proper order
  manageable data flow
source ports dynamically assigned, > 1023

## Slide 19: TCP
TCP Header Format

## Slide 20: TCP Illustration

## Slide 21: TCP Flags
URG: Urgent pointer field is significant in this segment
ACK: Acknowledgement field is significant in this segment
PSH: Push function
RST: Resets the connection
FIN: No more data from sender
SYN: Synchronize sequence numbers to initiate a connection

## Slide 22: TCP Connection Establishment
Client
Server
SYNn
SYNm, ACKn+1
ACKm+1

## Slide 23: TCP Connection Termination
Client
Server
FINn,ACKm
ACKn+1
ACKm+1
FINm,ACKn+1

## Slide 24: TCP Connection States
LISTENING: The socket is listening for incoming connections.
SYN_SENT: The socket is actively attempting to establish a connection.
SYN_RECV: A connection request has been received from the network.
ESTABLISHED: The socket has an established connection.
FIN_WAIT1: The socket is closed, and the connection is shutting down.
FIN_WAIT2: Connection is closed, and the socket is waiting for a shutdown from the remote end.

## Slide 25: TCP Connection States
TIME_WAIT: The socket is waiting after close to handle packets still in the network.
LAST_ACK: The remote end shut down, and the socket is closed. Waiting for acknowledgement.
CLOSING: Both sockets are shut down but we still don't have all our data sent.
CLOSE_WAIT: The remote end has shut down, waiting for the socket to close.
CLOSED: The socket is not being used.
UNKNOWN: The state of the socket is unknown.

## Slide 26
Client
Server
SYNn
SYNm, ACKn+1
ACKm+1
FINn,ACKm
ACKn+1
ACKm+1
FINm,ACKn+1
SYN_SENT
LISTENING
SYN_RCVD
ESTABLISHED
ESTABLISHED
FIN_WAIT1
CLOSE_WAIT
LAST_ACK
FIN_WAIT2
CLOSING
TIME_WAIT
CLOSED
CLOSED
Data Communication …

## Slide 27: Common Port Numbers
HTTP:80, DNS:53, FTP:21, HTTPS:443, …
Reference:
  Internet Assigned Number Authority (IANA) Port Numbers http://www.iana.org/assignments/port-numbers
  DNS Server: # nslookup –q=txt 80.tcp.portsdb.org # nslookup –q=txt 53.udp.portsdb.org # nslookup –q=txt icq.tcp.portsdb.org # nslookup –q=txt domain.udp.portsdb.org

## Slide 28: Application Layer
User process cooperating with another process on the same or different host
E.g.
  HTTP, SMTP, DNS, FTP, …

## Slide 29: Application Layer - HTTP
GET / HTTP/1.1 Accept: */* Accept-Language: en-us,zh-hk;q=0.5 Accept-Encoding: gzip, deflate User-Agent: Mozilla/4.0 (…) Host: www.ust.hk Connection: Keep-Alive Cookie: WTO_CLIENT=1
GET /en/index.html HTTP/1.1 Accept: */* Accept-Language: en-us,zh-hk;q=0.5 Accept-Encoding: gzip, deflate If-Modified-Since: Thu, 15 Jan 2004 06:21:45 GMT; length=208 User-Agent: Mozilla/4.0 (…) Host: www.ust.hk Connection: Keep-Alive Cookie: WTO_CLIENT=1
HTTP/1.1 200 OK Date: Sat, 03 Jul 2004 12:01:30 GMT Server: Apache/1.3.12 (Unix) mod_ssl/2.6.3 OpenSSL/0.9.5a Last-Modified: Tue, 25 Jun 2002 09:59:10 GMT ETag: "1a0a64-e4-3d183eee“ Accept-Ranges: bytes Content-Length: 228 Keep-Alive: timeout=15, max=100 Connection: Keep-Alive Content-Type: text/html
<data……>
HTTP/1.0 304 Not Modified Date: Sat, 03 Jul 2004 12:01:27 GMT Server: Apache/1.3.27 (Unix) mod_ssl/2.8.12 OpenSSL/0.9.6b ETag: "439a3-d0-40063179"

## Slide 30: Application Layer - SMTP
220 imsmq09.netvigator.com ESMTP Sendmail 8.12.10/8.12.10; Sat, 3 Jul 2004 20:17:39 +0800
HELO DEMO
250 imsmq09.netvigator.com Hello pcd633218.netvigator.com [218.102.165.218], pleased to meet you
MAIL FROM: <sender@netvigator.com>
250 2.1.0 <sender@netvigator.com>... Sender ok
RCPT TO: <receiver@cs.ust.hk>
250 2.1.5 <receiver@cs.ust.hk>... Recipient ok
RSET
250 2.0.0 Reset state
MAIL FROM: <sender@netvigator.com>
250 2.1.0 <sender@netvigator.com>... Sender ok
RCPT TO: <receiver@cs.ust.hk>
250 2.1.5 <receiver@cs.ust.hk>... Recipient ok
DATA
354 Enter mail, end with "." on a line by itself
.
250 2.0.0 i63CHdJe015428 Message accepted for delivery
QUIT
221 2.0.0 imsmq09.netvigator.com closing connection

## Slide 31: Presentation Layer – SMTP
Message-ID: <006f01c460f7$bbf3c440$6401a8c0@Jeep>
From: "Sender" <sender@netvigator.com>
To: "Receiver" <receiver@cs.ust.hk>
Subject: Demo
Date: Sat, 3 Jul 2000 20:17:36 +0800
MIME-Version: 1.0
Content-Type: multipart/mixed;
boundary="----=_NextPart_000_006C_01C4613A.C7BFF4E0"
This is a multi-part message in MIME format.
------=_NextPart_000_006C_01C4613A.C7BFF4E0
Content-Type: text/plain;
charset="big5"
Content-Transfer-Encoding: 7bit
Vincent IP
------=_NextPart_000_006C_01C4613A.C7BFF4E0
Content-Type: image/bmp;
name="my tiredness graph.BMP"
Content-Transfer-Encoding: base64
Content-Disposition: attachment;
filename="my tiredness graph.BMP"
Qk1KlgAAAAAAAEoAAAAoAAAAfAEAAMgAAAABAAQAAAAAAAAAAAB0EgAAdBIAAAUAAAAFAAAA////
… … …
------=_NextPart_000_006C_01C4613A.C7BFF4E0--

## Slide 32: Session Layer – SSL
CONNECTED(00000790)
depth=2 /C=US/O=VeriSign, Inc./OU=Class 3 Public Primary Certification Authority
Certificate chain
… … …
Server certificate
… … …
No client certificate CA names sent
SSL handshake has read 2769 bytes and written 330 bytes
---
New, TLSv1/SSLv3, Cipher is RC4-MD5
Server public key is 1024 bit
SSL-Session:
Protocol : TLSv1
Cipher : RC4-MD5
Session-ID: 0000E554D99EB7AA5858585858585858585858585858585840E6A6CA00000285
Session-ID-ctx:
Master-Key: D708B9C625E3183AE8E48D18723BE2ECE0E73F6A366283D07A34D69604D1AA15………
Key-Arg : None
Start Time: 1088857802
Timeout : 300 (sec)
Verify return code: 19 (self signed certificate in certificate chain)
---
[ CAN USE HTTP PROTOCOL HERE! ]

## Slide 33: Wireless Technologies
PAN
(Personal Area Network)
LAN
(Local Area Network)
WAN
(Wide Area Network)
MAN
(Metropolitan Area Network)
 | PAN | LAN | MAN | WAN
Standards | Bluetooth | 802.11 HiperLAN2 | 802.11 MMDS, LMDS, WiMAX | GSM, GPRS, CDMA, 2.5-3G
Speed | < 1Mbps | 11 to 54 Mbps | 11 to 100+ Mbps | 10 to 384Kbps
Range | Short | Medium | Medium-Long | Long
Applications | Peer-to-Peer Device-to-Device | Enterprise networks | T1 replacement, last mile access | Mobile Phones, cellular data

## Slide 34: WLAN IEEE 802.11 Standards
802.11 | Descriptions
802.11a | 5GHz, 54Mbps
802.11b | 2.4GHz, 11Mbps
802.11c | Wireless Bridging
802.11d | Multiple regulatory domains
802.11e | QoS and streaming extensions for 802.11a/g/h
802.11f | Roaming for 802.11a/g/h Inter Access Point Protocol IAPP (Access Point Interoperability)
802.11g | 54 Mbps WLAN in the 2.4 GHz band
802.11h | Dynamic Frequency Selection (DFS) and Transmit Power Control (TPC) (Interference)
802.11i | Authentication and Encryption (Security)
802.11j | Japan 802.11a additional Channels (4.9-5.1 GHz)
802.11k | Exchange of capability information between client and access point
802.11m | “Maintenance”, publication of standard updates
802.11n | Next Generation WLAN with at least 100 Mbps
802.11ac | Developed by 2013 and labelled as WiFi 5
802.11ax | Published in Feb 2021 and labelled as WiFi 6 (1 – 6 GHz) and WiFi 6E (5.925 GHz – 7.125 GHz).
802.11be | To be adopted by 2024 and labelled as WiFi 7
Notes: https://en.wikipedia.org/wiki/IEEE_802.11ax
https://en.wikipedia.org/wiki/IEEE_802.11ac-2013
https://www.tp-link.com/us/wifi-6e/

## Slide 35: Network Layers in Wireless LAN

## Slide 36: Basic Wi-Fi Network
Two basic components
  Access Points (AP) or Gateways.
    Base stations - A bridge between wireless and wired networks
    Wired network interface and Bridging software
    Aggregates access for multiple wireless stations to wired network
  Radio
    Aggregates access for multiple wireless stations to wired network. Wi-Fi radios
    Embedded or attached to the PCs (e.g.: USB)
    Notebooks embedded or with PCMCIA
    Mobile devices

## Slide 37: Infrastructure Mode
An access point (AP) is a shared device
Performance issues of shared hubs
Bridges allow for interconnection
Protocols/ applications work seamlessly

## Slide 38: Wireless Security Focus Areas
Authenticity
  Via BSSID (Basic Service Set ID), SSID, Wireless Encryption Scheme
Confidentiality
  Via encryption, Wireless Encryption Scheme
Integrity
  Via Wireless Encryption Scheme
From “Hacking Exposed Wireless 2nd Edition”

## Slide 39: WLAN Authentication Concept
802.11 Authentication
Non-cryptographic
Cryptographic (RC4)
Open System Authentication
Closed System Authentication (with SSID)
Identity based
Challenge-Response
Can join network with
empty SSID
Can join network
with valid SSID
Need SSID and WEP / WPA / WPA2

## Slide 40: WiFi settings
http://www.wi-fiplanet.com
Notes: http://www.wi-fiplanet.com/img/2005/09/ap_wpapsk.gif

## Slide 41: WiFi security related settings
http://www.howtogeek.com/204697/wi-fi-security-should-you-use-wpa2-aes-wpa2-tkip-or-both/
Notes: http://www.howtogeek.com/204697/wi-fi-security-should-you-use-wpa2-aes-wpa2-tkip-or-both/

## Slide 42: Wireless Network Attack – Getting SSID

## Slide 43: How to find hidden SSID
Get it from the access point
2. Get it from the client

## Slide 44
I am here
I am here
I am here
I am here
Beacon Frames

## Slide 45
Not Hidden
Hidden

## Slide 46
Is “sMobile” here?
Is “GovWifi” here?
Is “home”here?
Probe Request

## Slide 49: WEP Attack and Password Attack

## Slide 50: Password Cracking
You need a dictionary

## Slide 51: WEP Cracking

## Slide 52: Stream Cipher Reuse Example
From: https://cryptosmith.com/2008/05/31/stream-reuse/
A XOR K
B XOR K

## Slide 53: Stream Cipher Reuse Example
From: https://cryptosmith.com/2008/05/31/stream-reuse/
(A XOR K) XOR (B XOR K) = A XOR B

## Slide 54
What can I do…
If I have both SSID & Password
Decrypt the wifi traffic