## Slide 1: Processor security
COMP 4634
Some slides borrowed from Dan Boneh

## Slide 2: The processor
Part of the trusted computing base (TCB):
but is optimized for performance, … security may be secondary
Processor design and security:
Important security features: hardware enclaves, memory encryption (TME), RDRAND, and others.
Some features can be exploited for attacks:
  Speculative execution, transactional memory, …
Notes: TME: total memory encryption. Defends against dual-port memory DIMM, and cold boot attacks.

## Slide 3: Intel SGX / TDX
An overview
Software Guard eXtensions (SGX) Trust Domain eXtensions (TDX)
Also AMD SME and SEV
Notes: AMD SME (secure memory encryption) and SEV (secure encrypted virtualization)

## Slide 4: SGX / TDX: Goals
Extension to Intel processors that support:
Enclaves: running code and memory isolated from the rest of system (code outside of enclave cannot read enclave memory)
Attestation: prove to a remote system what code is running in the enclave
Minimum TCB: only processor is trusted, nothing else!
RAM and peripherals are untrusted
⇒ Memory controller must encrypt all writes to RAM (TME)
Why do we need this proof?
Notes: TME: total memory encryption

## Slide 5: Why enclaves 1: cloud computing
Goal: move data & VM to the cloud, without cloud seeing them in the clear
Simple solution: encrypt data and VM, key stays with Client
The problem: now cloud cannot search or compute on data
⇒ defeats the purpose of cloud computing
Client
Cloud (AWS, GCP, …)
Virtual Machine
(VM)
private data
Why?

## Slide 6: A solution: a HW enclave
Cloud (AWS, GCP, …)
hardware
hypervisor
TDX Isolated VM
private code and data
Goal: no one can read the memory of the isolated VM;
not the hypervisor, and not even a malicious admin
An unprotected VM
hypervisor can read memory
How does this work? Will see in a minute.
Notes: Trust Domain eXtensions (TDX)

## Slide 7: Why enclaves 2: protecting keys
Storing a Web server HTTPS secret key:
secret key is only available in the clear inside an enclave
⇒ malware cannot extract the key
web server
web server process memory
enclave
code
SGX isolated memory pages: only enclave code can read
OS, malware, and admin cannot read key
Web server code and data
OS and malware can read these addresses
Notes: How does web server use the key? Must call into enclave code with a request to use the key.

## Slide 8: Intel SGX: how does it work?
An application defines part of itself as an enclave
Process memory
Regular (non-isolated) memory

## Slide 9: How does it work?
An application defines part of itself as an enclave
Process memory
Enclave
create enclave
isolated memory in process memory space
Regular (non-isolated) memory

## Slide 10: How does it work?
An application defines part of itself as an enclave
Enclave
create enclave
call TrustedFun
enclave code runs
using enclave data
67g35bd954bt
Process memory
Regular (non-isolated) memory
enclave memory:
only readable
by enclave code
exit enclave
code here cannot read enclave memory
Notes: Data is stored encrypted in DRAM. Processor prevents access to data in cache outside of enclave.

## Slide 11: How does it work?
Part of process memory holds the enclave:
Process memory
app
code
OS
low
high
enclave
enclave
code
enclave
data
Processor prevents access to cached enclave data outside of enclave.
Enclave code and data are written encrypted to RAM (TME)
Notes: TME: total memory encryption

## Slide 12: Creating an enclave: new instructions
ECREATE: establish memory address for enclave
EADD: copies memory pages into enclave
EEXTEND: computes hash of enclave contents (256 bytes at a time)
EINIT: verifies that hashed content is properly signed
if so, initializes enclave (signature = RSA-3072)
EENTER: call a function inside enclave
EEXIT: return from enclave
Enclave init code loaded as cleartext

## Slide 13: When to send secret data to enclave: attestation
The problem: How does a remote system know when it can trust an enclave with its data?
Remote Attestation (simplified):
enclave
Intel’s app enclave
Intel’s quoting enclave
pk, report
pk, sk
cert = [pk, report]
report: contains hash(code)
validate cert
E(pk, data)
data
sk
remote server

## Slide 14: SGX Summary
An architecture for managing secret data
Intended to process data that cannot be read by anyone, except for code running in enclave
Attestation: proves what code is running in enclave
Minimal TCB: nothing trusted except for main processor
  ⇒ Memory controller encrypts all writes to RAM
Not suitable for legacy applications: must split app into parts
  Requires lots of code rewriting … not suitable for legacy apps

## Slide 15: TDX Briefly: an easy-to-use encalve
TDX: puts an entire VM in an enclave (e.g., an entire web server)
Support for attestation and minimal TCB (as with SGX)
Isolated VMs are managed by a new Intel TDX Module
  The TDX module is implemented in signed code by Intel
  It is loaded into an isolated region of physical memory
  Creates, manages, and attests to isolated VMs
https://cdrdv2.intel.com/v1/dl/getContent/690419
Notes: SEAM: Secure-Arbitration Mode

## Slide 16: One more example application
Data science on federated data:
MPC protocol
dataset1
dataset2
Can we run analysis on union(dataset1, dataset2) ??
cryptographic solutions (e.g., MPC) work for simple computations
result

## Slide 17: An example application
Data science on federated data:
dataset1
dataset2
For more complex analysis, can use (secure) hardware enclave
enclave
analysis code
pk, cert
pk, cert
E(pk, data1)
E(pk, data2)
untrusted environment
Cert includes hash of enclave code

## Slide 18: An example application
Data science on federated data:
dataset1
dataset2
For more complex analysis, can use (secure) hardware enclave
enclave
data1
data2
pk, cert
pk, cert
E(pk, data1)
E(pk, data2)
result
Cert includes hash of enclave code

## Slide 19: SGX insecurity: (1) side channels
Attacker controls the OS. OS sees lots of side-channel info:
Memory access patterns
State of processor caches as enclave executes
State of branch predictor
processor
OS
enclave
DRAM memory
memory bus
(enc data)
All can leak enclave data.
Difficult to block.

## Slide 20: SGX insecurity: (2) extract quoting key
Attestation: proves to 3rd party what code is running in enclave
Quoting sk stored in Intel enclave on untrusted machines
What if attacker extracts sk from some quoting enclave?
Can attest to arbitrary non-enclave code
… see Foreshadow attack and Intel’s response
Intel’s quoting enclave
attestation
data
sk

## Slide 21: The Spectre attack
Speed vs. security in HW
[slides credit: Paul Kocher]

## Slide 22: Performance drives CPU purchases
Clock speed maxed out:
  Pentium 4 reached 3.8 GHz in 2004
  Memory latency is slow and not improving much
To gain performance, need to do more per cycle!
  Reduce memory delays ⟶ caches
  Work during delays ⟶ speculative execution

## Slide 23: Memory caches (4-way associative)
Caches hold local (fast) copy of recently-accessed 64-byte chunks of memory
MAIN MEMORY
Big, slow
e.g. 16GB SDRAM
Set | Addr | Cached Data ~64B
0 | F0016280 31C6F4C0 339DD740 614F8480 | B5 F5 80 21 E3 2C.. 9A DA 59 11 48 F2.. C7 D7 A0 86 67 18.. 17 4C 59 B8 58 A7..
1 | 71685100 132A4880 2A1C0700 C017E9C0 | 27 BD 5D 2E 84 29.. 30 B2 8F 27 05 9C.. 9E C3 DA EE B7 D9.. D1 76 16 54 51 5B..
2 | 311956C0 002D47C0 91507E80 55194040 | 0A 55 47 82 86 4E.. C4 15 4D 78 B5 C4.. 60 D0 2C DD 78 14.. DF 66 E9 D0 11 43..
3 | 9B27F8C0 8E771100 A001FB40 317178C0 | 84 A0 7F C7 4E BC.. 3B 0B 20 0C DB 58.. 29 D9 F5 6A 72 50.. 35 82 CB 91 78 8B..
4 | 6618E980 BA0CDB40 89E92C00 090F9C40 | 35 11 4A E0 2E F1.. B0 FC 5A 20 D0 7F.. 1C 50 A4 F8 EB 6F.. BB 71 ED 16 07 1F..
Addr: 2A1C0700
Data: 9E C3 DA EE B7 D3..
Addr: 132E1340
Address:
132E1340
Data: AC 99 17 8F 44 09..
Addr: 132E1340
Data: AC 99 17 8F 44 09..
hash(addr) to map to cache set
132E1340
Evict to make room
AC 99 17 8F 44 09..
MEMORY
CACHE
2A1C0700
Data:
AC 99 17 8F 44 09..
CPU
Sends address, Receives data
Reads change system state:
Read to newly-cached location is fast
Read to evicted location is slow
Fast
Slow
Fast

## Slide 24: Speculative execution
  if (uncached_value == 1) // load from memory
  a = compute(b)
CPUs can guess likely program path and do speculative execution
  Example:
  Branch predictor guesses if() is ‘true’ (based on prior history)
  Starts executing compute(b) speculatively
  When value arrives from memory, check if guess was correct:
      Correct: Save speculative work ⇒ performance gain
      Incorrect: Discard speculative work ⇒ no harm
????
Notes: Prior history: branch predictor.

## Slide 25
Speculative Execution
CPU regularly performs incorrect calculations, then deletes mistakes
Architectural Guarantee
Register values eventually match result of in-order execution
Is making + discarding mistakes the same as in-order execution?
The processor executed instructions that were not supposed to run !!
The problem: instructions can have observable side-effects

## Slide 26: Conditional branch (Variant 1) attack
if (x < array1_size)
y = array2[ array1[x]*4096 ];
Suppose unsigned int x comes from untrusted caller
Execution without speculation is safe:
  array2[array1[x]*4096] not eval unless x < array1_size
What about with speculative execution?

## Slide 27: Conditional branch (Variant 1) attack
Before attack:
  Train branch predictor to expect if() is true (e.g. call with x < array1_size)
  Evict array1_size and array2[] from cache
if (x < array1_size)
y = array2[array1[x]*4096];
Memory & Cache Status
array1_size = 00000008
Memory at array1 base:
8 bytes of data (value doesn’t matter) Memory at array1 base+1000:
09 F1 98 CC 90...(something secret)
array2[ 0*4096]
array2[ 1*4096]
array2[ 2*4096]
array2[ 3*4096]
array2[ 4*4096]
array2[ 5*4096]
array2[ 6*4096]
array2[ 7*4096]
array2[ 8*4096]
array2[ 9*4096]
array2[10*4096]
array2[11*4096]
Contents don’t matter
Uncached
Cached
  
only care about cache status

## Slide 28: Conditional branch (Variant 1) attack
if (x < array1_size)
y = array2[array1[x]*4096];
Memory & Cache Status
array1_size = 00000008
Memory at array1 base:
8 bytes of data (value doesn’t matter) Memory at array1 base+1000:
09 F1 98 CC 90...(something secret)
array2[ 0*4096]
array2[ 1*4096]
array2[ 2*4096]
array2[ 3*4096]
array2[ 4*4096]
array2[ 5*4096]
array2[ 6*4096]
array2[ 7*4096]
array2[ 8*4096]
array2[ 9*4096]
array2[10*4096]
array2[11*4096]
Contents don’t matter
Uncached
Cached
  
only care about cache status
Attacker calls victim with x=1000
Speculative exec while waiting for array1_size:
    Predict that if() is true
    Read address (array1 base + x) (using out-of-bounds x=1000)
    Read returns secret byte = 09 (in cache ⇒ fast )

## Slide 29: Conditional branch (Variant 1) attack
if (x < array1_size)
y = array2[array1[x]*4096];
Memory & Cache Status
array1_size = 00000008
Memory at array1 base:
8 bytes of data (value doesn’t matter) Memory at array1 base+1000:
09 F1 98 CC 90...(something secret)
array2[ 0*4096]
array2[ 1*4096]
array2[ 2*4096]
array2[ 3*4096]
array2[ 4*4096]
array2[ 5*4096]
array2[ 6*4096]
array2[ 7*4096]
array2[ 8*4096]
array2[ 9*4096]
array2[10*4096]
array2[11*4096]
Contents don’t matter
Uncached
Cached
  
only care about cache status
Attacker calls victim with x=1000
  Next:
  Request mem at (array2 base + 09*4096)
  Brings array2[09*4096] into the cache
  Realize if() is false: discard speculative work
proceed to next instruction

## Slide 30: Conditional branch (Variant 1) attack
if (x < array1_size)
y = array2[array1[x]*4096];
Memory & Cache Status
array1_size = 00000008
Memory at array1 base:
8 bytes of data (value doesn’t matter) Memory at array1 base+1000:
09 F1 98 CC 90...(something secret)
array2[ 0*4096]
array2[ 1*4096]
array2[ 2*4096]
array2[ 3*4096]
array2[ 4*4096]
array2[ 5*4096]
array2[ 6*4096]
array2[ 7*4096]
array2[ 8*4096]
array2[ 9*4096]
array2[10*4096]
array2[11*4096]
Contents don’t matter
Uncached
Cached
  
only care about cache status
Attacker calls victim with x=1000
Attacker: (another process or core)
for i=0 to 255: measure read time for array2[i*4096]
When i=09 read is fast (cached), reveals secret byte !!
Repeat with x=1001,1002,… (10KB/s)

## Slide 31: Violating JavaScript’s sandbox
index will be in-bounds on training passes, and out-of-bounds on attack passes
JIT thinks this check ensures index < length, so it omits bounds check in next line. Separate code evicts length for attack passes
Do the out-of-bounds read on attack passes!
Keeps the JIT from adding unwanted bounds checks on the next line
Leak out-of-bounds read result into cache state!
Need to use the result so the operations aren’t optimized away
“|0” is a JS optimizer trick (makes result an integer)
if (index < simpleByteArray.length) {
index = simpleByteArray[index | 0];
index = (((index * TABLE1_STRIDE)|0) & (TABLE1_BYTES-1))|0;
localJunk ^= probeTable[index|0]|0;
}
4096 bytes = memory page size
Browsers run JavaScript from untrusted websites
  JIT compiler inserts safety checks, including bounds checks on array accesses
Speculative execution runs through safety checks…
Can evict length and probeTable from JavaScript (easy)
… then use timing to detect newly-cached location in probeTable

## Slide 32: Variant 2: indirect branches
Indirect branches: can go anywhere , e.g. jmp[rax]
  If destination is delayed, CPU guesses and proceeds speculatively
  Find an indirect jmp with attacker controlled register(s) … then cause mispredict to a useful ‘gadget’ y = array2[array1[x]*4096];
Attack steps:
  Mistrain branch prediction so speculative execution will go to gadget
  Evict address [rax] from cache to cause speculative execution
  Execute victim so it runs gadget speculatively
  Detect change in cache state to determine memory data

## Slide 33: Non-mitigations
Can we prevent Spectre without a huge cost in performance?
Idea 1: fully restore cache state when speculation fails.
Problem: Insecure!
Speculative execution can have observable side effects beyond the cache state
if (x < array1_size) {
y = array1[x];
do_something_observable(y);
}
occupy a bus: detectable from another core,
or cause EM radiation

## Slide 34
Variant 1 mitigation: Speculation stopping instruction (e.g. LFENCE)
  Idea: insert LFENCE on all vuln. code paths
if (x < array1_size)
LFENCE // processor instruction
y = array2[ array1[x]*4096 ];
LFENCE: stops speculative execution.

## Slide 35
Variant 1 mitigation: Speculation stopping instruction (e.g. LFENCE)
  Put LFENCES everywhere? ⇒ Abysmal performance
  Insert by smart compiler?
Transfer of blame (CPU -> SW): “you should have put an LFENCE there”
  Must protect against all potentially-exploitable patterns
  Supported in LLVM, along with other mitigations
  ⟹ protects all LLVM-based compilers
Notes: LLVM hardening: https://llvm.org/docs/SpeculativeLoadHardening.html

## Slide 36: Mitigations: summary
Mitigations are non-trivial for all Spectre variants:
  Software must deal with microarchitectural complexity
  Mitigations are hard to test:
        an active area of research (see Prof. Caroline Trippel’s work)
More ideas needed !

## Slide 37: ... but there is more
More speculative execution attacks:
Meltdown
Rogue inflight data load (RIDL) and Fallout
ZombieLoad
Micro-op caches (June 2020)
Pointer prefetching in Apple’s M1 (March 2024)
Enable reading unauthorized memory (client, cloud, SGX)
Mitigating incurs significant performance costs

## Slide 38: How to evaluate a processor?
Processors are measured by their performance on benchmarks:
Processor vendors add many architectural features to speed-up benchmarks
Until recently: security implications were secondary
⇒ lots of security issues found in last few years
… likely more will be found in coming years

## Slide 42: THE END